## Slide 1: ECE 273 – Computer Organization
Pre-labs for ECE 273
Created by Ranajeet Anand, Poornapragna Lakkoo, and Ryan Mattfeld, Spring 2013
Last Updated: 3/31/2013

## Slide 2: Laboratory 1 – Introduction to the Turbo Assembler

## Slide 3: Introduction to ECE 273
Two Main points of focus
  Teach the basics of Intel 8086 assembly language
    Assembly is the main link between high-level languages (like C and FORTRAN) and hardware
  Learn and reinforce proper commenting techniques when coding
    Program Headers
    Function Headers
    In-line Commenting

## Slide 4: Syllabus
Instructor Name: <Insert name here>
Instructor Email: <Insert email here>
Office Location: <Insert location here>
Office Hours: <Insert hours here>
Lab Manual can be found at:
  http://www.clemson.edu/ces/departments/ece/document_resource/undergrad/273Lab/ECE273.pdf
Grades
  Programming Effectiveness
  Commenting

## Slide 5: Mandatory Safety Video

## Slide 6: Laboratory 1 Tools
This lab uses 64 bit Macs for programming
  Will save programs using Xcode
The code we write will operate on 32 bit Linux machines
  We will use SSH to connect to 32 bit Linux machines in the basement of Riggs
We will compile using GCC
  EX: gcc –m32 C_code.c Assembly.s

## Slide 7: Preparations
Login using userid: eceuser and pass: riggs321
Open the terminal, and type “cesmount”, using your Clemson userid and password when prompted
  (This gives you access to your UNIX account storage.)
Then connect to a UNIX computer using SSH
  ssh userid@apolloXX.ces.clemson.edu
    XX can be from 01-16
Open X-Code, and using the toolbar on the top of your screen, create programs

## Slide 8: Instructions
For this week, the solution is given.
Create a C program in X-Code
  Copy the C code from the lab manual into the program you created
  Save file as <Filename>.c on your UNIX drive
Create an assembly program in X-Code
  Copy the Assembly solution from the lab manual into the program
  Save file as <Filename2>.s on your UNIX drive

## Slide 9: Preparations for Next Week
Read Lab 2 in the Lab Manual

## Slide 10: Laboratory 2 – Simple Assignments

## Slide 11: Introduction to Lab 2
To create assembly programs, some basic commands are necessary
  Creating Variables
  Modifying Variables
  Copying Variables

## Slide 12: Introduction to Lab 2
Registers are used to temporarily store data
  %eax, %ebx, %ecx, %edx are registers
Assembly can only perform one mathematical operation at a time:
  a = ((b + c) - (d + e)) - 10;
    movl b,%eax ; move b into register ax
    addl c,%eax ; add c to register ax
    movl d,%ebx ; move d into register bx
    addl e,%ebx ; add e to register bx
    subl %ebx,%eax ; subtract register bx from register ax
    subl $10,%eax ; subtract 10 from register ax
    movl %eax,a ; move register ax out to a

## Slide 13: Introduction to Lab 2
List of basic commands
  movl src, dst
    Copies value from src to dst
  addl src, dst
    Adds src to dst and stores the result in dst
  subl <number to subtract>, <subtract from>
    Subtracts the first value from the second value, storing the result in the second value

## Slide 14: Introduction to Lab 2
Tricky commands
  mull <value to multiply with %eax>
    “mull” only takes ONE value. It ALWAYS multiplies the value by the contents of register %eax
    The result is stored across two registers: %edx:%eax
    Two 4 byte numbers multiplied together can result in an 8 byte result
  divl <value to divide in to %edx:%eax>
    “divl” ALWAYS divides the 8 byte number created by combining %edx with %eax by the value given.
    This is so it can work properly with mull
  BE CAREFUL WITH THESE (25% of errors)

## Slide 15: Begin Lab 2
Review the lab manual (beginning assembly is difficult if you don’t understand the basic principles)
Read the “C” description of the function you will create in assembly
Review the “C” Code that runs the program and calls your function and copy the code into a C file.
Copy the assembly stub into an assembly file (save file with a “.s” ending)
Fill in the assembly as instructed to complete the function (due in 2 weeks)
Compare your results to those given in the manual

## Slide 16: Lab 3: Control statements

## Slide 17: Introduction
Objectives:
To introduce flags
To introduce jumps
To introduce conditional jumps
To introduce high-level control statements

## Slide 18: Introduction
In C:
Control statements like if..else.., while and for
In Assembly:
Conditional jumps
Unconditional jumps – equivalent of a ‘goto’ in C
Conditional jump possible by:
if (condition) then goto label
But how to evaluate if the condition is true or false?

## Slide 19: Introduction
Using Flags!
single bit of a special register in the CPU called the status register or flags register
Status (Flags) register:
3 main flags: zero flag, sign flag, and carry flag
Certain instructions cause these flags to be set according to the results of the instruction
A compare instruction (cmp) which sets the flags, without actually changing any of the other registers in the CPU

## Slide 20: Introduction
How Flags are set
Add instruction: result < 0
  Sign flag = 1, Zero flag = 0
Add instruction: result > 0
  Sign flag = 0, Zero flag = 0
Sub instruction: result = 0
  Sign flag = 0, Zero flag = 1
The carry flag indicates if a carry out occurred in the highest order bit position and thus is data dependent

## Slide 21: Introduction
Conditional Jumps:
jc label # jump if carry
jnc label # jump if not carry
js label # jump if sign
jns label # jump if not sign
jo label # jump if overflow
jno label # jump if not overflow
jpo label # jump if parity is odd
jpe label # jump if parity is even

## Slide 22: Introduction
Mostly these are necessary:
je label # jump if equal
jne label # jump if not equal
jg label # jump if greater than
jng label # jump if not greater than
jl label # jump if less than
jnl label # jump if not less than
jge label # jump if greater or equal
jnge label # jump if not greater or equal
jle label # jump if less or equal
jnle label # jump if not less or equal

## Slide 23: Introduction
The Compare instruction: cmp
The cmp instruction compares two values by subtracting the first operand from the second to set the flags.
Then the flags can be checked in order to determine the relationship between the two values
Used along with a jump instruction ‘j__’ to evaluate conditions like
if ( a > b ) then… else …

## Slide 24: Control Statements
If statement:
int a, b;
if (a > b) {
... code block ...
}
... more code ...
Assembly:
.comm a, 4
.comm b, 4
movl a, %eax
cmpl b, %eax
jng label
... code block ...
label:
... more code ...
If a > b then we do NOT want to jump, but we do want to execute the code block. The cmp instruction subtracts b from %eax and checks result of subtraction

## Slide 25: Control Statements
If-Else statement:
int a, b;
if (a > b) {
... code block ...
} else {
... code block 2 ...
}
... more code ...
Assembly:
.comm a, 4
.comm b, 4
movl a, %eax
cmpl b, %eax
jng else
... code block 1 ...
jmp more
else:
... code block 2 ...
more:
…more code …

## Slide 26: Control Statements
While loop:
int a, b;
while (a > b) {
... code block ...
}
... more code ...
Assembly:
.comm a, 4
.comm b, 4
while: movl a, %eax
cmpl b, %eax
jng more
... code block 1 ...
jmp while
more:
…more code …

## Slide 27: Control Statements
For loop:
int a, b;
for (i = 0; i < 100; i++)
{
... code block ...
}
... more code ...
Assembly:
.comm i, 4
movl $0, i
for: cmpl $100, I
jnl more
... code block 1 ...
cont: inc i
jmp for
more:
…more code …

## Slide 28: Control Statements
Do-while loop:
int a, b;
do{
... code block ...
} while( a > b)
... more code ...
Assembly:
.comm a, 4
.comm b, 4
do:
... code block 1 ...
cont: movl a, %eax
cmpl b, %eax
jg do # not negated
more:
…more code …

## Slide 29: Control Statements
Do-while loop:
int a, b;
while( a > b) {
... code block ...
}
... more code ...
Assembly:
.comm a, 4
.comm b, 4
while: movl a, %eax
cmpl b, %eax
jng more
... code block 1 …
movl %eax, a
jmp while
more:
…more code …
In all loops it is important that the loop variable be written to memory just before the jump back to the top so that when it is checked by the compare statement the correct value is used.

## Slide 30: Introduction
Break: using ‘jmp more’
Continue:
jmp cont for for and do loops
jmp while for while loops.

## Slide 31: Conditional Expressions
C Code:
int a,b,c,d;
if ((a + b) == (c - d)){
... code block 1 ...
}
... more code ...
Assembly:
.comm a, 4
.comm b, 4
.comm c, 4
.comm d, 4
movl a, %eax
addl b, %eax
movl c, %ebx
subl d, %ebx
cmpl %ebx, %eax
jne more
…code block 1..
more:
…more code …

## Slide 32: AND Expressions
int a,b,c,d;
if (a > b && c < d){
... code block 1 ...
}
... more code ...
is same as:
if (a > b){
if(c < d ){
... code block 1 ...
}
}
... more code ...
.comm a, 4
.comm b, 4
.comm c, 4
.comm d, 4
movl a, %eax
cmpl b, %eax
jle more:
movl c, %eax
cmpl d, %eax
jge more
…code block 1..
more:
…more code …
Break down multiple conditions separated by the && operator into nested if statements in C and then translate to assembly

## Slide 33: OR Expressions
int a,b,c,d;
if (a > b || c < d){
... code block 1 ...
}
... more code ...
is same as:
if (a <= b){
if(c >= d ){
goto more
}
}
... code block 1 ...
more:
... more code ...
.comm a, 4
.comm b, 4
.comm c, 4
.comm d, 4
movl a, %eax
cmpl b, %eax
jg code:
movl c, %eax
cmpl d, %eax
jl code
code:
…code block 1..
more:
…more code …
Take the inverse logic by using the property:
~(a or b) = ~a and ~b

## Slide 34: The Loop Instruction
C Code:
int i;
do {
... code block 1 ...
} while (--i);
... more code ...
Assembly:
.comm i, 4
movl i, %ecx
do:
…code block 1..
loop do
more:
…more code …
This instruction is used in loops that down count to 0 and sets the 0 flag and decrements loop index
- Loop index should be in %ecx which is a count register

## Slide 35: Lab 4: addressing modes Arrays and pointers

## Slide 36: Introduction
Addressing mode: how the computer selects the data that in an instruction
Data and Operands:
addl $4, %eax,
- Data: numerical values, i.e. 4
- Operand: symbol %eax and number 4

## Slide 37: Introduction
An “addressing mode” describes the relationship between the operands and the data.
Six Addressing Modes:
Immediate Addressing
Register Addressing
Direct Addressing
Indexed Addressing
Register Indirect Addressing
Base Indexed Addressing

## Slide 38: Addressing Modes
Immediate Addressing: Data is supplied as part of instruction
addl $10, %ecx
Register Addressing: Data is contained within a register
movl %eax, %ebx

## Slide 39: Addressing Modes
3. Direct Addressing: Memory address of the data is supplied with the instruction.
- an address is assigned by the compiler to the variable while translating the program to executable machine code
movl %eax, var #var = memory variable

## Slide 40: Addressing Modes
Declaring arrays in assembly:
int a[10]; /* an array of 10 integers */
.comm a, 40
- declares ten long words of memory and initializes them all to zero. a is a symbol that is equal to the address of the first word
Using the “fill” construct:
.fill 10, 4, 0 #Sets all elements to 0
Set the first 3 elements to the values 1,2,3 and the rest to zero
.int 1, 2, 3
.fill 7, 4, 0

## Slide 41: Addressing Modes
Accessing array elements: Direct addressing!
movl $10, a => a[0] = 10;
movl $5, a+12 => a[3] = 5;
- 12 is added as offset since 12 = 3x4 where 3 is the array index and 4 is size of integer
- Direct addressing is preferred to access fixed array indexes
- Suppose address of a is 4096, then we can write
movl 4096, %eax #load a[0] in %eax
- but better to use the label a than using absolute address since the address is calculated by the compiler

## Slide 42: Addressing Modes
4. Indexed Addressing
- Access a[i], that is, variable array index
Use the contents of a register along with the displacement to compute the memory address of the data
Displacement: base address of the array or array label
Register: hold the array index. Two special index registers: %esi and %edi are used.
%esi: source index and %edi: destination index
movl i, %edi
movl $30, a(,%edi,4) # a[i] = 30;

## Slide 43: Addressing Modes
5. Register Indirect Addressing: The %ebx register holds the address of the data to be addressed
int *p;
*p = 40;
Assembly code would be:
.comm p, 4
movl p, %ebx
movl $40, (%ebx)
Pointers can be stored in any register except %esp
Pointer stored in memory should be moved to a register before we can use it as a pointer.

## Slide 44: Addressing Modes
6. Base Indexed Addressing: Specify 2 registers
  %ebx which holds the base address of the array
  %esi or %edi, which holds the index.
  If the array is an array of records, a constant offset may also be specified
  Suppose we have:
  int *ap;
  struct {
  int a, b;
  } *asp;
  int i;

## Slide 45
C code:
ap[3] = 50;
ap[i] = 60;
asp[i].b = 70;
Assembly Code:
.comm ap, 4
.comm asp, 4
.comm i, 4
. . .
movl ap, %ebx
movl $50, 12(%ebx) # ap[3] = 50;
movl i, %edi
movl $60, (%ebx, %edi, 4) # ap[i] = 60;
movl asp, %ebx # i is still in di
movl $70, 4(%ebx, %edi, 4) # asp[i].b = 70;

## Slide 46: Addressing Modes
Final Note:
Accessing array variables can be done by using %esi, %edi, and %ebx interchangeably.
The only place this is not true is when specifying two registers (base indexed mode): one of the registers must be %ebx
There is a distinction between a base register, which holds a pointer, and an index register which is used to compute an offset from the base.

## Slide 47: Summary
Recap of addressing modes:
Immediate Addressing
movl $4, %eax
Register Addressing
  movl %eax, %ebx
Direct Addressing
movl %eax, var
movl %eax, var+12

## Slide 48: Summary
Recap of addressing modes:
Indexed Addressing
movl $30, a(,%edi,4)
- Register Indirect Addressing
  movl $40, (%ebx)
Base Indexed Addressing
movl $60, (%ebx, %edi, 4)

## Slide 49: Lab 5: Subroutines and the Stack

## Slide 50: Introduction
Writing and calling subroutines
Stack organization

## Slide 51: Subroutines
What are subroutines?
Code segment that performs a specific task.
In assembly, any label can be a subroutine.
2. How to use the subroutines?
Use unconditional jump instruction – jmp label_name to go to the label. Use another unconditional jump – jmp next_statement to return to the next statement after first jump.
b. Use call and ret instruction.

## Slide 52: Subroutines
C code –
main()
{
.
.
func1();
.
.
}
func1()
{
}
Assembly using jmp –
main:
.
.
jmp func1;
nxt_st : .
.
func1: .
.
jmp nxt_st;
Assembly using call –
main:
.
.
call func1;
.
.
func1: .
.
ret
No label on next statement.
How does ‘ret’ know where to return to?

## Slide 53: Call instruction
What is different in the call usage? What extra information would the assembler need to use the call and ret instruction?
There is no need for a label on the statement after the function call.
Instead, with the “call” instruction, the return address (the statement after the call) is ‘remembered’.
2. How is the return address remembered?
Return address is ‘push’ed onto a special segment of memory called Stack.
Address of the statement immediately after call.
call func1;
RA : .
.

## Slide 54: Stack
What is a Stack?
Stack is a special data structure.
2. What are the uses of Stack?
a. Retain base addresses as is after a function has returned.
b. Store “Return Address” after a “call” instruction.
c. Parameter passing between functions.
3. How to access the Stack?
push and pop instructions. push – adds a new value to the stack
pop – removes a data value from the stack.
Base Addresses
Return Address
Parameters

## Slide 55: Registers of the Stack
ess - > Stack Segment Register
- Points to the part of memory where stack starts.
esp - > Stack Pointer Register
- Points to the top of the stack(location where the last data is stored on stack).
ebp - > Base Pointer Register
- Points to the base of a stack frame.
Data
Data
Data
Data
ess ->
0
4
8
12
16
20
24
28
32
36
40
44
esp ->
Stack

## Slide 56: Push and Pop instructions
push
Example : pushl $10
Data
Data
Data
Data
ess ->
0
4
8
12
16
20
24
28
32
36
40
44
esp ->
Stack

## Slide 57: Push and Pop instructions
push
Example : pushl $10
Step 1 – Decrement esp
Data
Data
Data
Data
ess ->
0
4
8
12
16
20
24
28
32
36
40
44
esp ->
Stack

## Slide 58: Push and Pop instructions
push
Example : pushl $10
Step 1 – Decrement esp
Step 2 – Push 10 onto stack
10
Data
Data
Data
Data
ess ->
0
4
8
12
16
20
24
28
32
36
40
44
esp ->
Stack

## Slide 59: Push and Pop instructions
2. pop
Example : popl %eax
Data
Data
Data
Data
ess ->
0
4
8
12
16
20
24
28
32
36
40
44
esp ->
Stack
Stack is as it was before ‘push’ instruction.
But if ‘push’ instruction is executed, stack will be as in previous slide.

## Slide 60: Push and Pop instructions
2. pop
Example : popl %eax
Step 1 – pop top of stack to operand
Data
Data
Data
ess ->
0
4
8
12
16
20
24
28
32
36
40
44
esp ->
Stack
operand cannot be a constant like in push

## Slide 61: Push and Pop instructions
2. pop
Example : popl %eax
Step 1 – pop top of stack to operand
Step 2 – Increment esp
eax = 10.
Data
Data
Data
ess ->
0
4
8
12
16
20
24
28
32
36
40
44
esp ->
Stack
operand cannot be a constant like in push

## Slide 62: CALL instruction
Back to call instruction
What happens when call is executed?
Step 1. The return address is pushed onto the stack
Step 2. A jump is made to the label provided.
Ex :
pushl RA;
call func; jmp func;
RA : <Next statement>;
RA
Data
Data
Data
ess ->
0
4
8
12
16
20
24
28
32
36
40
44
esp ->
Stack

## Slide 63: Local variables and Stack Frame
When a call is entered and exited, ideally we want the registers to retain their original values.
But the new function might need the registers for their own functions.
SOLUTION – push all the needed registers onto the stack and create your own space for local variables. The space on the stack for local variables is called the “stack frame”.
Base registers – ebp and ebx are the registers usually pushed onto the stack to retain base addresses.
How to do this?
prolog and epilog

## Slide 64: PROLOG and EPILOG
prolog
pushl %ebp
pushl %ebx
movl %esp, %ebp
subl $SIZE_OF_LOCAL_VARS, %esp
esp to ebp is the “stack frame” and the size is dependent on the number of local variables.
Also, ebp is the new base pointer register for stack operations.
Size of local variables . .
OLD_ebx
OLD_ebp
RA
Data
Data
Data
ess ->
0
4
8
.
.
20
24
28
32
36
40
44
esp ->
Stack at end of prolog
ebp ->

## Slide 65: PROLOG and EPILOG
epilog
movl %ebp, %esp
popl %ebx
popl %ebp
ret
OLD_ebx
OLD_ebp
RA
Data
Data
Data
ess ->
0
4
8
12
16
20
24
28
32
36
40
44
esp ->
Stack at end of epilog
Stack returned to original state after epilog.
at ret, RA is popped and the program returns back.
Need not be erased. It may remain on stack.

## Slide 66: Lab 6: Subroutine parameters

## Slide 67: Subroutine Parameters.
Passing parameters to functions
Method 1 – Using registers
Disadvantages –
Limited
Understanding between calling function and called function needed.
Method 2 – Using the stack
Advantages over register method –
More parameters can be passed.
Less understanding between the calling function and called function needed.
How to use stack for parameters?
Simply push the parameters onto the stack from the calling function
In the called function, remember how stack is rearranged in prolog and access the parameters by an offset to ebp register.

## Slide 68: Subroutine Parameters
int a,b,c,d;
main()
{
d = func(a,b,c);
}
int func(int p1,int p2, int p3)
{
return p1+p2+p3;
}
main:
/* prolog */
pushl c;
pushl b;
pushl a;
call func;
func;
/*prolog*/
/*access “a” first then “b”, then “c” according to the number of bytes in prolog and RA.
Pushed in reverse order.

## Slide 69: Subroutine Parameters
Size of local variables . .
OLD_ebx
OLD_ebp
RA
Parameter1 = a
Parameter2 = b
Parameter3 = c
ess ->
0
4
8
.
.
20
24
28
32
36
40
44
esp ->
Stack at end of prolog
ebp ->
func:
pushl %ebp;
pushl %ebx;
movl %esp,%ebp;
subl $LOCAL,%esp;
movl 12(%ebp),eax;
addl 16(%ebp),eax;
addl 20(%ebp),eax;
movl %ebp,%esp;
popl %ebx;
popl %ebp
ret;
Offset is
size(RA + OLD_ebp +OLD_ebx) = 4+4+4 = 12
Put return value in eax register.

## Slide 70: Subroutine Parameters
Return statement
Using the return statement, a value can be returned back to the calling function.
In assembly, the return value is always placed in eax. There is an understanding between the calling function and the called function that the return value will be in the eax register.

## Slide 71
THE END